## Slide 1
MP5 MiniClaw
From Wrong Requirements to Honest Design
David Ricciotti • Haben Berhe • Yoel Tesfatsion
ME 493B | RobotExpo 2026 | ACME Robotics

## Slide 2
The Brief
What Jordan asked us to build
Jordan Chen Design Brief — MP1
Compete with Hiwonder's BigClaw at RobotExpo 2026
Envelope: 92 × 46 × 55 mm
Grip target: close on a ~25 mm object
Thumb-wheel turns: 2–3 from open to closed
Grip force: 5–8 N
Material: FDM PLA (Prusa MK4S)
Part count: < 15 parts
Cost: < $3/unit at 500-unit scale
Note: brief states no jaw opening — team set ≥40 mm as a self-imposed target
"The BigClaw outsells us 3-to-1. Your MiniClaw has to feel just as capable in a package about 20% smaller."
— Jordan Chen, Engineering Manager

## Slide 3
Where We Ended Up
Final MiniClaw design vs. targets (MP1 + team)
Specification | Target | Final Design | Status
Jaw opening | ≥ 40 mm (team) | 40.13 mm | Met
Envelope | 92 × 46 × 55 mm | 92 × 46 × 55 mm | Met
Thumb-wheel turns | 2–3 | 0.28 | Renegotiated
Gear stress SF | ≥ 2.0 | 2.14 | Met
Part count | < 15 | 25 | Over target
Trans. angle margin | > 0° above 40° | 21.3° margin | Met

## Slide 4
The Renegotiation Story
GOAL & DIRECTION
Why we accepted 0.28 turns instead of 2–3
Architecture B (compound spur)
N = 16 → 1.24 thumb-wheel turns
Center distance: 126 mm total
Exceeds 92 mm housing by 34 mm
Part count: 29 (5 gears)
Packaging: DOES NOT FIT
Architecture A (single spur pair)
N = 1 → 0.28 thumb-wheel turns
Center distance: 20 mm
Fits easily in 92 mm housing
Part count: 25 (2 gears)
Packaging: SOLVED

## Slide 5
When Context Was Missing
CONTEXT MGMT
One document upload corrected the entire design basis
Parameter | AI Without Context | After MP1 Brief Upload
Jaw opening target | 40 mm | 25 mm
Input range | 0°–46° | 0°–28°
Link lengths | L1=40, L2=20 | L1=12, L2=26
Displacement | 20.3 mm/side | 12.5 mm/side
Lesson learned:
The AI will confidently build on wrong assumptions if you don't provide the requirements document. Context management isn't optional.
Also missing early: Haben's repo was private (403) until made public. Yoel's MP4 Part A arrived late — his linkage (24 mm jaw, μ=57°–119°) confirmed Haben's design as the right selection.

## Slide 6
Our Stack
TOOLS & INTEGRATION
Tool | Used For
Devin (Cognition AI) | Part A notebooks, Part B templates, plots, stress analysis, 12+ PRs
GitHub Copilot (agent) | Haben's Part A, David's MP3 gear CAD
MiniClaw Gear DFM Skill | Yoel's MCP RAG server + ACME corpus (ACME-ENG-001, MFG-002)
matplotlib / numpy | Comparison plots, linkage simulation, drive-train sketch
GitHub | Version control, code review, team integration
Live demo coming up: animated four-bar simulation + compute_transmission_angle() on perturbed geometry

## Slide 7
The Pin Clearance Loop
CENTAUR ENGINEERING
Human × AI = something neither would have produced alone
David asked: "What bore diameter gives a reliable sliding fit after FDM tolerance?"
Bore Ø (mm) | Designed | FDM Offset | Post-FDM | Verdict
3.20 | 0.20 mm | −0.20 mm | 0.00 mm | INTERFERENCE
3.30 | 0.30 mm | −0.20 mm | 0.10 mm | Tight
3.40 | 0.40 mm | −0.20 mm | 0.20 mm | RELIABLE FIT
Human: FDM tolerance data from MP1 AI: systematic clearance stack calculation
Result: bore increased to Ø3.40 mm across all 10 joints. No reaming needed.

## Slide 8
The Wrong-AI Moment
EVALUATION & TRUST
What the AI claimed
Designed David's linkage targeting: • 40 mm jaw opening • 0°–46° input range • L1=40, L2=20 link lengths Complete design with position equations, transmission angle analysis, motion plots, and hand calculations. Everything checked out internally.
What was actually true
David's MP1 Part B design used: • ~25 mm jaw opening (to grip a ~25 mm object) • 0°–28° input range • L1=12, L2=26 link lengths The AI had never seen David's MP1 work. It guessed the specs and built a plausible-looking but wrong design.
How we caught it
David compared the AI's output against his original design brief. The numbers didn't match. One document upload fixed everything. Mechanism: the human knew the requirements. The AI didn't.
Context management isn't optional — it's the difference between a correct design and a plausible-looking wrong one.

## Slide 9
Per-Subsystem Trust Assessment
EVALUATION & TRUST
Subsystem | Flag | Print Tomorrow? | Key Issue
1. Linkage | Needs work | YES | Strongest analytically (3-path verified)
2. Drive Train | Needs work | YES | SF = 2.14, but 0.28 turns untested ergonomically
3. Jaw Arms | Unknown | NO | No CAD exists
4. Housing | Unknown | NO | No CAD exists
5. Input Wheel | Unknown | NO | No CAD exists
6. Pins | Needs work | YES | Ø3.40 bore designed; test one joint first
Bottom line: Not ready to print a complete gripper. Three subsystems are analytically solid; three have no CAD. This is an honest assessment.

## Slide 10
What We'd Do Differently
1. Shared team repo from Day 1
Cross-repo integration (cloning Haben's private repo, cloning Yoel's repo, extracting parameters) added friction. A single shared workspace from the start would have eliminated the 403 errors, the manual data extraction, and the integration PRs.
2. Build the MCP tool call earlier
Having compute_transmission_angle() live during linkage selection (Loop 1) would have made the comparison interactive instead of static. The tool we demo today should have existed in Week 4.

## Slide 11
Live Demo
Yoel Tesfatsion
Part 1: Dynamic Simulation
Haben's four-bar linkage sweeping −50° to +50°
Jaw opening from 0 to 40 mm and back
Transmission angle staying in workable band
Real-time data display
Part 2: Live Tool Call
compute_transmission_angle(L3=32)
vs. our design (L3=29)
Shows angle drops with 3 mm change
Tool catches bad geometry instantly
$ Terminal
$ python3 linkage_simulation.py $ python3 transmission_angle_check.py --- Haben's design --- μ range: 61.3° – 91.3° Margin: 21.3° above 40° --- Perturbed: L3=32 --- μ range: 56.0° – 84.1° Margin: 16.0° above 40°

## Slide 12
Questions?
Pillar | Answerer
Goal & Direction | David Ricciotti
Context Management | Haben Berhe
Tools & Integration | Yoel Tesfatsion
Centaur Engineering | Haben Berhe
Evaluation & Trust | David Ricciotti
Thank you!